## Slide 1
Dynamic Channel Allocation for IoT Networks Using Interference-Aware Wi-Fi
👉 SYSTEMS / NETWORK OPTIMIZATION PROJECT

## Slide 2
INTRODUCTION
  IoT devices mostly rely on Wi-Fi (2.4 GHz) for communication
  Multiple IoT nodes + routers share limited channels
  Static channel selection causes:
  High interference
  Packet loss
  Increased latency
  Dynamic Channel Allocation (DCA) solves this by continuously adapting the channel based on interference

## Slide 3
PROBLEM STATEMENT
Static Channel Allocation
  One channel is selected at startup
  Channel remains fixed even if congestion increases
  Results in:
    Poor throughput
    Higher retransmissions
    Energy wastage in IoT nodes
Need
  IoT networks need self-adapting communication
  Channels should change automatically when interference increases

## Slide 4
2.4 GHz Band
  Total channels: 13
  Only 3 non-overlapping channels: 1, 6, 11
  High interference due to:
    Bluetooth
    Microwaves
    Nearby Wi-Fi networks
WI-FI BANDS & CHANNELS OVERVIEW

## Slide 5
Core Idea of the Project
Interference-Aware Dynamic Channel Allocation
  IoT node does not stick to one channel
  It:
Monitors current channel quality
Scans other channels
Selects the least congested channel
Switches connection without manual intervention

## Slide 6
Methodology
Step 1: Initial Channel Connection
  IoT device connects to a default Wi-Fi channel
  Starts normal data transmission
Step 2: Continuous Monitoring
  Measures:
    Signal strength (RSSI)
    Noise level
    Packet loss
Step 3: Wait & Observe Phase
  Device waits for a fixed time window
  If interference stays below threshold → continue
  If interference exceeds threshold → scan

## Slide 7
Step 4: Channel Scanning
  Device scans all available bands
  For each channel:
    Checks number of active networks
    Measures interference level
    Computes channel score
Step 5: Free / Best Channel Detection
  A channel is considered free if:
    Low interference
    Low network traffic
Methodology

## Slide 8
Step 6: Channel Switching
  If a better channel is found:
    Disconnect from current channel
    Reconnect to new channel
  Ensures:
    Minimal packet loss
    Seamless communication
Step 7: Resume Data Transmission
  IoT node continues normal operation
  Monitoring restarts (loop)
Methodology

## Slide 9
Role:
Creates the Wi‑Fi network (DynamicAP) that all devices connect to. It starts on channel 1 and listens for HTTP commands to change the operating channel.
Key Functions:
  Wi‑Fi AP Mode: Hosts a network with SSID “DynamicAP”, password ”password”.
  Channel Control Endpoint: Provides /setchannel?channel=X – receives channel change commands from the controller and attempts to switch.
  Status Endpoint: /status – reports the current channel to the controller (used for synchronisation).
  No Channel Scanning: The AP itself does not scan; it simply follows orders from the controller.
Interaction:
  Receives HTTP GET requests from the controller to change channel.
  All other devices (controller, IoT node) connect to this AP
Access Point (wifi)

## Slide 10
Role:
  The brain of the system. Periodically scans all Wi‑Fi channels (1‑11), computes an interference score for each, decides if a channel switch is beneficial, and commands the AP to switch. It also hosts a real‑time dashboard and a UDP echo server for latency measurement.
Key Functions:
    Channel Scanning: Every 30 seconds, performs a passive scan of channels 1‑11, counting APs and measuring RSSI.
    Interference Scoring: Calculates a score for each channel based on:
      Number of APs (1 point each)
      Number of strong APs (RSSI>‑70 dBm, 2 points each)
      Adjacent channel interference (±1 ch: 0.5×APs, ±2 ch: 0.25×APs)
      Preference for non‑overlapping channels 1,6,11 (score multiplied by 0.8)
Central Controller

## Slide 11
  Decision Logic: Compares the best channel’s score with the current channel’s score; switches only if the best is at least 20% better.
  Web Dashboard: Serves a web page at http://192.168.4.2/ showing current channel, latency, packet loss, and per‑channel scores (auto‑refresh every 5 s).
  UDP Echo Server: Listens on port 8888, echoes back any received packet (used by IoT node to measure RTT).
  Metrics API: /api/node-metrics accepts latency and loss reports from the IoT node (via GET or POST via Http).
  JSON Status API: /api/status provides all real‑time data for the Python collector(format).
Interaction:
  Sends HTTP /setchannel commands to the AP.
  Receives UDP packets from the IoT node and echoes them.
  Receives HTTP metrics from the IoT node.
  Serves web dashboard to any connected browser.
  Provides JSON data to the external Python collector.

## Slide 12
example live analysis in http

## Slide 13
IoT Node
Role:
  Simulates an IoT device that generates regular traffic and reports network performance metrics (latency, packet loss) back to the controller. These metrics help evaluate the impact of channel changes.
Key Functions:
  UDP Traffic Generation: Every second, sends a UDP packet to the controller (port 8888) containing a sequence number and a timestamp.
  Echo Detection: Listens for the echoed packet, calculates round‑trip time (RTT), and increments a counter for acknowledged packets.
  Metrics Computation: Every 10 seconds, computes:
  Average latency = total RTT / number of echoes received.
  Packet loss (%) = (sent packets – acknowledged packets) / sent packets × 100.
  HTTP Reporting: Sends the computed metrics to the controller’s /api/node-metrics endpoint (using GET with query parameters).
  Static IP: Configured with IP 192.168.4.3 for reliable communication.
Interaction:
  Sends UDP packets to controller and receives echoes.
  Sends HTTP metrics to controller.
  All traffic goes through the AP (ESP32 #1).

## Slide 14
Flow diagram
Adaptive Frequency Hopping

## Slide 15
Results

## Slide 19
Advantages of Proposed System
  Reduced interference
  Improved throughput
  Lower packet loss
  Energy-efficient IoT nodes
  Self-adaptive network behavior

## Slide 20
Applications
  Smart homes
  Smart factories
  IoT sensor networks
  Campus Wi-Fi IoT deployment
  Healthcare monitoring systems

## Slide 21
Conclusion
  Static channel allocation is inefficient for dense IoT networks
  Interference-aware dynamic allocation improves performance
  System adapts automatically to changing network conditions
  Suitable for real-world IoT deployments